## Slide 1
Guillaume NOETINGER
Postdoc
Laboratory of Wave Engineering (LWE)
Prof. Romain Fleury
EPFL- STI – IEM
An introduction to analogue optical computing

## Slide 2: Why analog computing ?
Image generation:
Optimization:
Protein folding:
But also material design,
algorithm design etc…

## Slide 3: Motivation
Modern technologies can be useful and fun…
A photo of a teddybear on a skate board in Time Square
DALL-E 2 OpenAI
They can also raise significant concerns
Source: AI Index report, Stanford University (2024)
Increasing
complexity
Increasing
energetic
consumption
Notes: Wave engineering is a very interdisciplinary field because wave phenomenon, be it of mechanical nature such as sound, or EM nature such as light, can transfer energy and information over many ranges of distances and in many media. So we’re very broad and I’ll show you very diverse ecamples of the impact of our research in various fields.

## Slide 4: AI and computing
graph: https://openai.com/index/ai-and-compute/
animation from Google Research
Need: x300 000 over 5 years
Moore: x7 only
Notes: Double every three month, to be compared with Moore’s law (doubles every 2 years). Over the past 5 years, the compute needs grew by 300 000, while Moore’s law provided only a factor of 7 in our capacities.

## Slide 5: End of Moore’s law
Moore’s law : doubling in transistor number every two years
16 to 7 nm:
160 to 70 atoms !
Claims for a
transistor <2nm
(< 20 atoms) IBM, 2021
Alternative for enhancing computing capacities ?
Atomic limit + Limited heat evacuation !
Not deployed… ?

## Slide 6
“The world is rapidly running out of computing capacity”
Satya Nadella, CEO of Microsoft, Jan 2018
Notes: Not a sustainable trend

## Slide 7: Why analog computing was abandoned?
Analog computing with metamaterials,
F. Zangeneh-Nejad et al., Nature reviews materials, 2020
Mechanical
Analog electronics
Problem of speed and number of inputs/outputs
Problem of noise
Application specific
Notes: Historical perspective

## Slide 8: Why analog computing was abandoned?
Signal to Noise Ratio problem and specificity solved by the digital computer :
Memory access
= Von Neuman Bottleneck
John Von Neumann (1903-1957)
‘Von Neumann architecture’
Transistor
Boolean logic
Sequential logic
Flip-Flop
Programming
Integrated circuit
GPU: NVIDIA A 100
10 TeraFLOPS, 300W
TPU: 400 TeraFLOPS, 75W
Notes: Optimized for AI but remain Von Neuman machines

## Slide 9: The basis of actual (digital) computing
Noise/stochasticity + possible retroactions is to be mastered for alternative types of computing !
Hence a major focus on error correction codes e.g. for quantum computing…
Possible to get rid of noise
via thresholding
No degradation of signals
Possible to implement Boolean algebra
using only switches
A Symbolic Analysis of Relay and Switching Circuits,
Claude Shannon 1937
Input-Output
Isolation
Full Adder
Allows to make building block and
assemble them like Lego !

## Slide 10: Other computing paradigm
Neuromorphic Quantum Ising machines
Different physical implementations
Classification:
Character/Pattern recognition
Non-linear regression
Algorithmic:
Integer factorization
Graph search/classification
Adapted to ≠ algorithms to solve ≠ problems:
Examples:
NP-hard problems
Barahona F. On the complexity of Ising spin glass models. J Phys. (1982)
Binary optimization

## Slide 11: Outline
Differentiating signals with light:
  Two examples
  How it works (a small black board derivation)
  Applications
Solving equations with light
  Linear differential equations
  Integral equations and matrix inversions
  Implementing general matrix multiplications
Neuromorphic computing with light
  Deep neural networks
  Physical neural networks
  Physical learning systems
Conclusions: Opportunities and challenges for optical computing
How to implement basic
operations with light ?

## Slide 12: Taking the derivative with light:
Silva, Monticone, Castaldi, Galdi, Alù and Engheta, Science 343, 160, 2014
Zhu, Zhou, Lou, Ye, Qiu, Ruan and Fan, Nature Communications 8, 15391 (2017)
Notes: Double every three month, to be compared with Moore’s law (doubles every 2 years). Over the past 5 years, the compute needs grew by 300 000, while Moore’s law provided only a factor of 7 in our capacities.

## Slide 13: How can this work ?
transfer function
We set , with a slow enveloppe
We ideally want , possibly with delay
Is this possible, and under which conditions on ?
LTI optical system
reflection or transmission
Notes: Double every three month, to be compared with Moore’s law (doubles every 2 years). Over the past 5 years, the compute needs grew by 300 000, while Moore’s law provided only a factor of 7 in our capacities.

## Slide 14: Let’s explore it together!
Show that
Show that
Would a unitary transfer function work ?
Would a non-unitary transfer function work ?
Notes: Double every three month, to be compared with Moore’s law (doubles every 2 years). Over the past 5 years, the compute needs grew by 300 000, while Moore’s law provided only a factor of 7 in our capacities.

## Slide 15: Conclusions
We need with and
Computation occurs at the Wigner-Eisenbud time-delay
But: significant power is lost in the process: prone to noise
time t can be replaced by space, x ( becomes )
Notes: Double every three month, to be compared with Moore’s law (doubles every 2 years). Over the past 5 years, the compute needs grew by 300 000, while Moore’s law provided only a factor of 7 in our capacities.

## Slide 16: Differentiating in time
Sol, del Hougne, Smith, Meta-programmable analog differentiator, Nature communications 13, 1713 (2022)
Notes: Double every three month, to be compared with Moore’s law (doubles every 2 years). Over the past 5 years, the compute needs grew by 300 000, while Moore’s law provided only a factor of 7 in our capacities.

## Slide 17: Differentiation of optical pulses
Huang, Zheng, Dong, Gao, and Zhang, "Terahertz-bandwidth photonic temporal differentiator based on a silicon-on-isolator directional coupler," Opt. Lett. 40, 5614-5617 (2015)

## Slide 18: Differentiating in spatial domain
Zhu, Zhou, Lou, Ye, Qiu, Ruan and Fan, Nature Communications 8, 15391 (2017)
Zhou et al., Natl Sci Rev, Volume 8, Issue 6, June 2021, nwaa176
Differentiator + microscope
Zhu, Zheng, Kravchenko and Valentine,
Nature Communications 14, 316 (2020)
Notes: Right : Photonic crystal + BIC (guided mode with high Q)

## Slide 19: Differentiation and integration
Brewster angle
Differentiate:
Integrate:
Zangeneh-Nejad, Fleury, Analogue computing with metamaterials, Nat. Rev. Mater. 6, 207 (2021)

## Slide 20: Outline
Differentiating signals with light:
  Two examples
  How it works (a small black board derivation)
  Applications
Solving equations with light
  Linear differential equations
  Integral equations and matrix inversions
  Implementing general matrix multiplications
Neuromorphic computing with light
  Deep neural networks
  Physical neural networks
  Physical learning systems
Conclusions: Opportunities and challenges for optical computing

## Slide 21: First order linear differential equations
First order ODE :
simple Lorentzian resonance
Yang et al., All-optical differential equation solver with constant coefficient tunable based on a single microring resonator, Sci Rep 4, 5581 (14).

## Slide 22: Arbitrary-order differential equations
n-th order ODE :
sum of 1st order ODE
Solving a 2nd order ODE with acoustic waves
Zangeneh-Nejad, Fleury, Topological analogue signal processing, Nature Communications 10, 2058 (2019).

## Slide 23: How about more complex equations
What we can solve so far: , i.e. any convolution
A broader family of integral equations are the Fredholm integral equations of the second kind:
If the Fourier trick does not work anymore…
ex: Solve for the Kernel: on
This belongs a family of integral equations called Fredholm integral equations of the first kind,
Input
Kernel

## Slide 24: Kernel discretization
becomes a matrix and the problem
becomes a matrix-vector equation:
K
Solution (Neumann series):
Initial guess
Send , get , add to
Update , Iterate
Solve roughly at Wigner-Smith time
Mathematical operations and equation solving with reconfigurable metadevices, Tzarouchis et al., Light: Science & Applications 2022

## Slide 25: All we need: matrix vector multiplications
photonic
crossbar arrays
Pb: requires SVD decomposition
MZI meshes
Pb: complexity
Notes: Double every three month, to be compared with Moore’s law (doubles every 2 years). Over the past 5 years, the compute needs grew by 300 000, while Moore’s law provided only a factor of 7 in our capacities.

## Slide 26: Example with MZI
Essentially just implements a controllable function

## Slide 27: Brute force inverse design of
Guided accumulation of active particles by topological design of a second-order skin effect, Lucas S. Palacios, Nat Comm 2021
Multi-dimensional data transmission using inverse-designed silicon
photonics and microcombs, KY Yang et al. Nat Comm 2022

## Slide 28: Optics experiment
500 nm
Cordaro, A., Edwards, B., Nikkhah, V. et al. Solving integral equations in free space with inverse-designed ultrathin optical metagratings. Nat. Nanotechnol. 18, 365–372 (2023)

## Slide 29: Outline
Differentiating signals with light:
  Two examples
  How it works (a small black board derivation)
  Applications
Solving equations with light
  Linear differential equations
  Integral equations and matrix inversions
  Implementing general matrix multiplications
Neuromorphic computing with light
  Wave propagation & fully connected neural network
  Training a wave-based device
  Going full-field
Conclusions: Opportunities and challenges for optical computing

## Slide 30
Wave propagation vs. fully connected neural network
Deep learning with coherent nanophotonic circuits,Y. Chen et al, 2017, Nat. Phot. 2017
Diffraction
by a slit
Complex media
Strong analogy between propagation of waves and the propagation of signals in a neural network
Arthur Gower @University of Sheffield
How digital neural networks
are trained ?
Large datasets
backpropagation (scalable)
Non-linearity is essential
N Vidia: “An estimate is that 80% to 90% of the cost of machine learning at scale devoted to AI is due to inference rather than training”
”On average, a chatGPT prompt consumes 10 times more than the same inquiry on Google”.
Notes: The seminal experiment

## Slide 31: Inference in integrated photonics
Pai et al., Experimentally realized in situ backpropagation for deep learning in photonic neural networks, Science 380, 6643 (2023)
Miller, Fan groups.

## Slide 32
Advantage of waves for computing
The physics of optical computing
P. McMahon, Nat. Rev. Phys 2023
Waves perform complex calculations passively
Controled from modifiying of the propagation media.
Optics has a particularly large spatial and temporal bandwidth
500nm light in 5 cm
= 1015 indept modes
5cm wafer
= 1011 transistors
Quasi-lossless Fourier
optical processing
through a 4f correlator
Parallelism
>300 THz bandwidth
1 operation
= 1 pulse
potentially 100 000x
higher than electronics
optical system
Wigner-Eisenbud scattering time
optical fan in,
with a lens

## Slide 33: Scaling: opportunities and challenges
Anderson, Ma, Wang, Wright, Mc Mahon, Optical transformers, arXiv 2302.10360 (2023)
We need 108 parameters to gain x100 advantage in energy efficiency using optics compared to state of the art GPU.
SLM:
N2=2Mp,
rate=17ms (1/60Hz)
1matrix multipl. =2N2-N = 4 Mop.
2.34 108 FLOP
GPU:
104 op./ns
1013 FLOPs

## Slide 34: The idea of physical neural networks
Deep learning is just about learning complex functions to perform a given task
Every controllable system implements a controllable function
Replace layers with physical systems with controllable weights
  challenge: how to implement a large number of tunable parameters
  solution 1: work with what you have, scale later
  solution 2: send the weights together with the input
Do not forget that non-linearity is key
  challenge: how to reconcile this with low-power operation
  solution 1: train for linear operations (ex: linear matrix multiplications)
  solution 2: Do not relate input and output by linear propagation through a medium (detector non-linearity, input vector encoded in the medium configuration)
Find ways to train efficiently
  challenge: Backpropagation scales well but requires a differentiable model
  solution: developp dedicated training schemes

## Slide 35
Training a wave-based device
Training of physical neural networks, Momeni et al, Nature (2025)
Backpropagation-free training of deep physical neural networks, Momeni et al., Science (2023)
Physical Local Learning
(PhyLL)
Forward-Forward algorithm
No backward pass
Physical system used
as an encoder
However it is not really robust to experimental noises
The workhorse of neural
network training:
Backpropagation
Physics Aware Training
(PAT)
Deep physical neural networks
trained with backpropagation,
Wright et al., Nature (2022)

## Slide 36: Training of PNNs – a brief overview
Momeni et al., Training of physical neural networks, Nature 2025

## Slide 37
Going full-field
All-optical machine learning using diffractive deep neural networks, Lin et al., Science 361, 1004 (2018)
Limited scalability of on-chip photonics + Lightwaves propagates in 3D
No full-field source in THz,
Obtained using superposition and XY scanning:
Very high SNR
Is it possible to engineer a similar experiment but in a reconfigurable way, in the visible range and in full-field ?
Could pave the way to
very compact devices
performing complex operations
passively.
Downscaling the wavelength:
to
+ Not the same engineering
precision of the propagation media
Trainable using PhyLL ?

## Slide 38
Reconfigurable free-field hardware: spatial light modulators
Liquid cristals
Deformable mirrors
Digital Micromirror Device (DMD)
≈ 100 d.o.f.s
(Not perfectly independent for a continuous surface)
Response time depends on the size
10Hz to 1 kHz actuation
(large vs. small variations)
Reflective or transmissive
≈ 2Mp (= d.o.f.s) resolution up to 16bits
≈ 100 Hz maximum refresh rate
Phase modulator or
amplitude modulator
(with a waveplate and a polarizer)
Reflective only
≈ 2Mp binary pixels (= d.o.f.) resolution.
≈ 10 kHz refresh rate
Various technologies adapted to different use !
vs. FLOPS for state-of-the art GPUs….
Notes: Come from the compensation of distorted atmospheric wavefront for astronomy

## Slide 39: Measuring and modifying large scattering matrices
Vellekoop, Mosk, Opt. Lett. 32, 23092311 (2007)
Review: Mosk, Lagendijk, Lerosey & Fink, Nature Photonics, 6, 283-292 (2012)

## Slide 40
Self-configuring high-speed multi-plane light conversion, Rocha et al. Nat. Com. 2025
Successive free-space propagation in a MPLC configuration
Multi Plane Light Converter
Spatial Light Modulator (SLM)
facing a mirror
Complicated alignment
+ slow optimization
Nonlinear processing with linear optics,
Yildirim et al. Nat. Phot. 2024
Fully linear propagation
How to add a
nonlinearity ?
Structural non-linearity

## Slide 41: Computing in linear cavities with nonlinear mapping
Nonlinear optical encoding enabled by recurrent linear scattering,
Xia et al., Nat. Phot (2024)
Notes: Double every three month, to be compared with Moore’s law (doubles every 2 years). Over the past 5 years, the compute needs grew by 300 000, while Moore’s law provided only a factor of 7 in our capacities.

## Slide 42
Mimicking free-space propagation using a 4f system
Spatial multiplexing to
speed up the
training process
Batch processing
Possible to use only two
SLMs
Non-linearity comes for free
from the camera readout !
SLM
SLM
Stacking
SLMs
Tutorial: A practical guide to the alignment of defocused spatial light modulators for fast diffractive neural networks, Noetinger & Tuuva, ArXiv 2025
100 epochs of 50k MNIST
examples @60 Hz
1 day of training
The images are pixels
vs. 1920x1200 pixels
resolution of SLMs

## Slide 43
Alignement procedure
Tutorial: A practical guide to the alignment of defocused spatial light modulators for fast diffractive neural networks, Noetinger & Tuuva, ArXiv 2025
How to ensure each image is processed exactly in the same way ?
µD
SLM
Sharp index changes
on the SLM are visible in a conjugated plane
Before
calibration
After
calibration
Raw images + Final fitting
Thresholded images for ellipse fitting
Concentric circles = dark disks
Robust to
defocus

## Slide 44
Tutorial: A practical guide to the alignment of defocused spatial light modulators for fast diffractive neural networks, Noetinger & Tuuva, ArXiv 2025
Alignement procedure
The noise among all channels
are slightly differents:
Averaging effect
Average
Before calibration:
After calibration:
Uniform illumination + Identical phase patterns: Random speckles
Slightly different speckle patterns
± identical speckles
Too
different
pattern
(SSIM)
Average
A ‘coherent’ sum
is retrieved

## Slide 45: The set-up
Input data xn
(amplitude modulator)
Weights (phase)
output data xn+1
(amplitude detector)
read-out non-linearity
0
1
2
3
6
7
8
9
5
4
Notes: donnée modulées envoyé par system 4f sur SLM
flèches vertes: polarization
Polarized beam splitter (lame 1/4 avant pour polarizer)
udisplay change la pola ce qui envoie vers la gauche
SLM a une pola horizontale donc on fait tourner avec une lame lda/2
1 pixel on SLM = 1 pixel on udisplay
un peu de pola verticale filtrée par un polarizer
diaphragme en plus pour atténuer le bruit/filtrer/ajuster les hautres fréquences spatiales (ajuster le grain d'un speckle)
DeltaZ ajuste pour ajuster le mélange des données
PSF1: airy spot quasi diffraction limited, can be neglected
PSF2: bessel-like function (multiplication by a Toeplitz matrix)
udisplay: amplitude mask, we do not use.
difference with Ozcan: finite spatial extension=filter by diffraction (not fully equaivalent to closeby SLMs)
limiting lens is L2
on pourrait utiliser une stack de SLM conjugués: cher + dégradation du SNR
au lieu on utilise 2 et on renvoie l'output dans l'input pour faire plusieurs layers + nonlinearité gratuite au niveau de la camera
on peut moduler les données en amplitudes (non fait) et en phase, on normalize donc on récupère le flux à chq layer

## Slide 46
Digital twin
We build a surrogate in-silico model to learn the relationship between inputs & outputs:
We use a U-net architecture such as:
Input
Phasemask
Output
Surrogate
0
1
0
2π
0
1
0
1
Convolution
+ Residual
Block
Convolution
+ Residual
Block
Spatial
Attention
Convolution
+ Residual
Block
Convolution
+ Residual
Block
Skip connections
Inputs
Output
+
Phase
masks

## Slide 47: A 16-channel free-space optical neural network
Images, phase masks,
propagation, and camera readout
are organized as a tiled optical field.
4 x 4
spatial channel array
5-6
optical phase layers
>1M
trainable phase values
Display
SLM
Camera
A. Momeni, G. Noetinger, T. Tuuva and RF, “Multi-channel optical vision model”, arXiv:2606.10253 (2026)
1: Physical output defines the loss signal
2: Surrogate gradients update phase masks
3: New optical pairs fine-tune the surrogate
2
1
3
4
6
5
10
9
11
7
8
12
14
13
15
16
2
1
3
4
6
5
10
9
11
7
8
12
14
13
15
16
2
1
3
4
6
5
10
9
11
7
8
12
14
13
15
16
Drift immune
training

## Slide 48: Hybrid Vision Language Model
Input image
Input and phase
encoding
(16 channels)
Surrogate model
Fine-tuning
Backward pass
Optical layers
Readout
Digital
Transformer
decoder
layers
Output text
Surrogate model
Forward pass
The man in the dark ….
Input text
The man in the ….
0.871
final eval caption loss
0.930
BLEU-1
0.848
BLEU-4
A. Momeni, G. Noetinger, T. Tuuva and RF, arXiv:2606.10253 (2026)

## Slide 49: Outline
Differentiating signals with light:
  Two examples
  How it works (a small black board derivation)
  Applications
Solving equations with light
  Linear differential equations
  Integral equations and matrix inversions
  Implementing general matrix multiplications
Neuromorphic computing with light
  Deep neural networks
  Physical neural networks
  Physical learning systems
Conclusions: Opportunities and challenges for optical computing

## Slide 50: Towards learned sensing
brain power consumption: 20W
analog data compression
SRC Decanal plan for semiconductors (2020, left), G. Courtine’s lab, EPFL (2023)
huge compressing costs for biomedical implants

## Slide 51: Thank you
Questions?
guillaume.noetinger@epfl.ch
romain.fleury@epfl.ch